## Slide 1: A Comparative Illustration of Trip- and Activity-Based Modelling Techniques
Hayden Atchley
Committee:
Greg Macfarlane (chair)
Grant Schultz
Gustavious Williams

## Slide 2: Travel Demand Models
2 main types:
Trip-based
  Aggregate
  Trips happen
Activity-based
  Synthetic population
  Trips result from decisions
Travel Demand Model
Trips | Vehicle-miles traveled
Volumes | Level of service

## Slide 3: Advantages of Activity-Based Models
Activity-based models thought to be superior:
Information on individuals
Trip chaining (tours)
Conceptually closer to reality
More detailed analysis
  Equity analyses

## Slide 4: Difficulties with Activity-Based Models
Computational complexity
Complicated design
Lack of interoperability
Staff training
Things may be changing
  Open-source models (ActivitySim)
  General maturity/familiarity

## Slide 5: Research Gap
Comparisons focus on theoretical benefits
Cited difficulties may be outdated
Practicality of activity-based models
  Ease of use
  Types of analyses
  Ease of interpretation

## Slide 6: Two Models
WFRC Model (trip-based)
ActivitySim (activity-based)
Notes: Introduce validation/calibration

## Slide 7: Model Calibration
Population
  Household size
  Income
Trips
  Mode choice
  Remote work
  Trip length distribution
Notes: We used Iteration 4.
We also validated on district population, income, TLFD, and remote work.

## Slide 8: Scenarios Overview
Land Use Scenario | Transit Scenario | Remote Work Scenario
New development at old Draper prison site Projected 2050 data for The Point development | Increase frequency and speeds of FrontRunner New Frontrunner stations Based on WFRC 2050 plan | Higher work-from-home and telecommute Calibrated to WFRC 2050 projections

## Slide 9: Land Use Scenario New development (The Point)
WFRC Model:
Change land use data for The Point area
  Match 2050 data
    7,430 new households
    22,200 new jobs
ActivitySim:
New synthetic population for The Point area
  Population modeled on Gateway area (SLC)
  Joined with baseline scenario population

## Slide 10: New Trips
WFRC Model
ActivitySim

## Slide 11: WFRC: Non–Home-Based Trips

## Slide 12: ActivitySim: New Resident Trips

## Slide 13: Transit Scenario Improved FrontRunner
WFRC Model:
Doubled train frequency
  Peak: 2 → 4 trains per hour
  Off-peak: 1 → 2 trains per hour
Used future speed and track extensions
  Additional stations in Vineyard, Springville, Spanish Fork, and Payson
ActivitySim
New transit skims from WFRC model

## Slide 14: Change in Mode Split

## Slide 15: At-Work Mode Switching
Notes: At-work trip modes of those who switched away from Drive Alone for work tours

## Slide 16: Daily Mode Switching

## Slide 17: Transit Riders Income Distribution
Notes: The WFRC Model is a distribution of (weighted) medians, and ActivitySim is a distribution of actual individual incomes.

## Slide 18: Remote Work Scenario Increased remote work rates
WFRC Model:
Used 2050 remote work rates
  Work-from-home average increase from 2.9% to 3.5%
  Telecommute average increase from 3.7% to 10.2%
ActivitySim:
Recalibrated remote work to WFRC 2050 rates
  Work-from-home matches WFRC data
  Telecommute matches % by job type

## Slide 19: Remote Work Considerations
“Rebound effect”
  Fewer work trips may cause more non-work trips
Trip length
  Longer commute more likely to work remotely
Household structure
  Single- vs. dual-parent
  Age of children
ActivitySim Work-From-Home Model

## Slide 20: Change in Number of Trips
Notes: The ABM has a “rebound effect” where there are mode HBO trips as a result of the increased remote work

## Slide 21: WFRC: Trip Count vs Length
Notes: For drive alone HBW trips, the % decrease in number was greater than in distance. This shows that on average shorter HBW trips were “dropped” with increased remote work.

## Slide 22: ActivitySim: Trip Count vs Length
Notes: Work trips show more decrease in length than in number of trips. This shows that longer work trips are being “dropped”, perhaps in exchange for shorter HBO trips.

## Slide 23: Conclusions
Cited difficulties with activity-based model:
Computational complexity
Complicated design
Lack of interoperability
Staff training
Notes: Limitless number of analyses, these are only examples. But for the same effort, more in-depth analysis with ActivitySim

## Slide 24: Conclusions
Computational complexity
  Similar runtime on same hardware
Complicated design
  Easier interpretation with activity-based
Lack of interoperability
  ActivitySim remote work sub-models taken from SEMCOG
  Simple to add/edit parameters
Staff training
  Similar time/effort between models
Cited difficulties may not be applicable!
Notes: Limitless number of analyses, these are only examples. But for the same effort, more in-depth analysis with ActivitySim